## Slide 1: Ellipsoid-Based Path Planning
Group Meeting
05/25/2018

## Slide 2: Highway Roadmap planner
C-Space Obstacles: Closed-form Minkowski Sum/Difference
  Affine Transformation (Shrinking) -> Shrunk Space
  Offset Curve
  Inverse Transform (Stretching)
Closed-form Minkowski Sum

## Slide 3: Highway Roadmap planner
Free-Space Characterizations
  Discretize Rotation
  Cell Decomposition: At each C-Layer
Edge Connections between Collision-free Vertices Within one layer
  Connect between adjacent cells
Between different layers
  Enlarge the robot, compute local c-space
  Intersection of two local c-space
Collision-free Cells and Roadmap in One Layer
Highway Roadmap Planner for 2D Rigid Body

## Slide 4
Enclose the robot by a slightly larger ellipsoid
Compute Minkowski Sum/Difference using the larger ellipsoid
  Robot can move inside free of collision
  Description of such motion formulates a “local c-space” for the vertex
  Lower bounds for allowable motion of an ellipsoid contained in another
New vertex at the intersection between the local c-space of two vertices
  Connect new vertex with the two original vertices respectively
Local C-space for Vertex Connections between Different Layers
Strategy to connect vertex between different C-layers
Layer i+1
Layer i
Robot
Result
Illustration of the problem

## Slide 5
Converting implementations from Matlab to C++
  Inputs: shape parameters for superquadrics obstacles, ellipsoid robot
  Minkowski Sum/Difference between ellipsoids and superquadrics
  Cell decomposition by sweep-line procedure
    boundary enlarging (-> polygon bounding boxes for c-obstacles)
    decompose to polygon cell
  Vertex connections within one layer
  Vertex connections between adjacent layers
    Minimum distance neighbors
    KC connection strategy
  Graph search (Dijkstra or A*)
Connect to MoveIt and benchmark algorithms
Current Work Summary

## Slide 6
Obtain environment shape parameters from point clouds
  Enclose points by superquadrics
  Compare with Oriented Bounding Box
    Metric: Efficiency and volume percentage of occupancy
Hybrid with PRM
  Sample the orientation
Test on a real holonomic mobile robot system
Other work in the near future