## Slide 1: Ellipsoid Motion Planning: “Highway Roadmap” planner
Sipu Ruan

## Slide 2: Motivations
Sample-based planners
  PRM, RRT, and their variants
  Efficient for high dimensional configuration space
  Require “sample-check-keep/reject” processes; Always fail in “narrow passage” problems
Can we explicitly parameterize free space and sample from it to reduce
  Number of collision-checking calculations
  Number of samples that are discarded
  Or even without any collision detection?
Deterministic planners using Poly-ellipsoids and Superquadrics to model the robots and environment
  Simple math expressions for describing the shapes
  Closed-form characterizations of Minkowski sums

## Slide 3: Highway Roadmap planner
Separation of translations and rotations
  Construct C-Layers (C-Slices)
Generation of C-Obstacles
  Closed-form Minkowski sum/difference
Detection of collision-free space
  “Raster-scan” process
Connections of collision-free vertices within one C-Layer
  Expand the boundary of obstacles to form convex (trapezoidal) collision-free cells
Connections of vertices among different C-Layers
  Concept of “Kinematics of Containment”
Finding feasible path from start to goal
  Graph search algorithms: Dijkstra, A*, etc

## Slide 4: Minkowski Sum/Difference
In general,

## Slide 5: Closed-form Minkowski Sum/Difference
Ellipsoid-Ellipsoid:
  Expressions:
  Shrinking:
  Offset surface:
  Surface normal:
  Transform back:
Y. Yan, G S. Chirikjian. Closed-form characterization of the Minkowski sum and difference of two ellipsoids. Geom Dedicata (2015) 177:103–128

## Slide 6: Closed-form Minkowski Sum/Difference
Ellipsoid-Superquadrics:
  Superquadrics:
    2D:
    3D:

## Slide 8: Highway Roadmap planner
Separation of translations and rotations
  Construct C-Layers (C-Slices)
Generation of C-Obstacles
  Closed-form Minkowski sum/difference
Detection of collision-free space
  “Raster-scan” process
Connections of collision-free vertices within one C-Layer
  Expand the boundary of obstacles to form convex (trapezoidal) collision-free cells
Connections of vertices among different C-Layers
  Concept of “Kinematics of Containment”
Finding feasible path from start to goal
  Graph search algorithms: Dijkstra, A*, etc

## Slide 9: Raster scan process
Generate collision-free line segments using set theory
Y. Yan, Q. Ma, and G S. Chirikjian, Path Planning Based on Closed-Form Characterization of Collision-Free Configuration-Spaces for Ellipsoidal Bodies, Obstacles, and Environments, RSS 2016

## Slide 10: Highway Roadmap planner
Separation of translations and rotations
  Construct C-Layers (C-Slices)
Generation of C-Obstacles
  Closed-form Minkowski sum/difference
Detection of collision-free space
  “Raster-scan” process
Connections of collision-free vertices within one C-Layer
  Expand the boundary of obstacles to form convex (trapezoidal) collision-free cells
Connections of vertices among different C-Layers
  Concept of “Kinematics of Containment”
Finding feasible path from start to goal
  Graph search algorithms: Dijkstra, A*, etc

## Slide 11: Connect vertices within one C-Layer
Conditions on collision-free cells

## Slide 12: Connect vertices within one C-Layer
Finding tangent line segments that circumscribe the curved boundary by trigonometry

## Slide 13: Highway Roadmap planner
Separation of translations and rotations
  Construct C-Layers (C-Slices)
Generation of C-Obstacles
  Closed-form Minkowski sum/difference
Detection of collision-free space
  “Raster-scan” process
Connections of collision-free vertices within one C-Layer
  Expand the boundary of obstacles to form convex (trapezoidal) collision-free cells
Connections of vertices among different C-Layers
  Concept of “Kinematics of Containment”
Finding feasible path from start to goal
  Graph search algorithms: Dijkstra, A*, etc

## Slide 14: Kinematics of containment
Allowable motion of an ellipsoid inside a slightly larger ellipsoid
  Find intersection of the two “local c-space” volumes

## Slide 15: Kinematics of containment
Closed-form lower bound of the KC volume
  Problem to be solved:
  Equivalent to:
Q. Ma, GS. Chirikjian. A CLOSED-FORM LOWER BOUND ON THE ALLOWABLE MOTION FOR AN ELLIPSOIDAL BODY AND ENVIRONMENT. ASME IDETC 2015

## Slide 16: Kinematics of containment
Q. Ma, GS. Chirikjian. A CLOSED-FORM LOWER BOUND ON THE ALLOWABLE MOTION FOR AN ELLIPSOIDAL BODY AND ENVIRONMENT. ASME IDETC 2015

## Slide 17: Kinematics of containment
Larger KC volume
  Convex optimization to find extreme points
    or equivaltently,
  Other extreme points:
    Fix one coordinate to be zero, compute extreme motion of the smaller ellipsoid

## Slide 18: Kinematics of containment
  Point-in-polyhedron test

## Slide 19: Highway Roadmap planner
Separation of translations and rotations
  Construct C-Layers (C-Slices)
Generation of C-Obstacles
  Closed-form Minkowski sum/difference
Detection of collision-free space
  “Raster-scan” process
Connections of collision-free vertices within one C-Layer
  Expand the boundary of obstacles to form convex (trapezoidal) collision-free cells
Connections of vertices among different C-Layers
  Concept of “Kinematics of Containment”
Finding feasible path from start to goal
  Graph search algorithms: Dijkstra, A*, etc

## Slide 20: Roadmap and valid path

## Slide 21: Future work
Compare with sample-based algorithms from popular motion planning library: OMPL
Hybrid method with sample-based planners
Extend to high dimensional C-Space